## Slide 1: LAB 3-2 Review
张佳豪

## Slide 2: 目录
Cache参数
优化前测试
消融优化
  nextline预取
  Non-Blocking Cache
  Victim Cache
  stride prefetch
  没有尝试的策略:Eviction Policy, Bypass
最终优化

## Slide 3: Cache参数
使用提供的镜像安装gcc-multilib和g++-multilib
编译cacti并按照配置修改cache.cfg文件运行

## Slide 4: Cache参数
默认配置下,32nm工艺节点下,L1 Cache的 Hit Latency
为(1.48)ns,约等于(3)cycle
默认配置下,32nm工艺节点下,L2 Cache的 Hit Latency 为
(1.92)ns,约等于(4)cycle

## Slide 5: 优化前测试
Metric | 01-mcf-gem5-xcg | 02-stream-gem5-xaa
L1 Total Reads | 181,708 | 113,651
L1 Total Writes | 50,903 | 49,245
L1 Write Misses | 5,002 | 6,159
L1 Miss Rate | 20.05% | 11.34%
L2 Total Reads | 46,628 | 18,473
L2 Read Misses | 22,247 | 18,473
L2 Miss Rate | 39.61% | 75.52%
Main Mem Reads | 22,247 | 18,473
Main Mem Writes | 2,535 | 4,624
Total Latency | 3,737,713 | 3,043,008
Average Latency | 16.07 | 18.68
Theoretical AMAT | 12.95 | 12.70
Simulated AMAT | 16.07 | 18.68
Notes: > 程序运行结果平均延时大于上面的数值。因为上面的数值使用公式计算，而模拟器是用总延迟除以总访问次数，其中包含了驱逐块的延迟.
> 即使将evict时间设置为0，模拟器的平均延迟也会大于理论值，因为统计的miss rate包含了驱逐操作，所以miss rate偏低.(驱逐dirty块写基本都会命中)
> 为了方便后续优化均采用Simulated AMAT

## Slide 6: nextline预取
Nexline预取采用miss时预取后n行的实现

## Slide 7: L1 Metrics Comparison (01-mcf trace)
Settings | L1 Miss Rate | Coverage Rate | Prefetch Accuracy
11 | 20.05% | N/A | N/A
21 | 18.59% | 25.3062% | 23.1318%
31 | 17.80% | 37.3026% | 18.8574%
41 | 17.63% | 42.5023% | 14.9348%
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行

## Slide 8: L1 Metrics Comparison (02-stream trace)
Settings | L1 Miss Rate | Coverage Rate | Prefetch Accuracy
11 | 11.34% | N/A | N/A
21 | 5.67% | 54.6459% | 99.9567%
31 | 3.78% | 69.7623% | 99.9351%
41 | 2.84% | 77.3205% | 99.9134%
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行

## Slide 9: L2 Metrics Comparison (01-mcf trace)
Settings | L2 Miss Rate | Coverage Rate | Prefetch Accuracy
11 | 39.61% | N/A | N/A
12 | 39.55% | 12.9184% | 22.9311%
13 | 39.23% | 23.4849% | 20.0833%
14 | 39.24% | 25.9774% | 16.4848%
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行

## Slide 10: L2 Metrics Comparison (02-stream trace)
Settings | L2 Miss Rate | Coverage Rate | Prefetch Accuracy
11 | 75.52% | N/A | N/A
12 | 37.77% | 49.9877% | 99.9567%
13 | 25.19% | 66.6462% | 99.9351%
14 | 18.89% | 74.9775% | 99.9134%
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行

## Slide 11: Combined Metrics (01-mcf trace)
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行
Configuration | AMAT | L1 Miss Rate | L2 Miss Rate | L1 Coverage Rate | L1 Prefetch Accuracy | L2 Coverage Rate | L2 Prefetch Accuracy
11 (Base) | 16.07 | 20.05% | 39.61% | N/A | N/A | N/A | N/A
22 (Opt1) | 14.81 | 18.59% | 26.86% | 0.253 | 0.231 | 0.321 | 0.968
33 (Opt1) | 13.99 | 17.80% | 20.87% | 0.373 | 0.189 | 0.465 | 0.957
44 (Opt1) | 13.64 | 17.63% | 16.85% | 0.425 | 0.149 | 0.538 | 0.948

## Slide 12: Combined Metrics (02-stream trace)
Setting中(XY)表示含访问的1行L1预取X行，L2预取Y行
Configuration | AMAT | L1 Miss Rate | L2 Miss Rate | L1 Coverage Rate | L1 Prefetch Accuracy | L2 Coverage Rate | L2 Prefetch Accuracy
11 (Base) | 18.68 | 11.34% | 75.52% | N/A | N/A | N/A | N/A
22 (Opt1) | 10.84 | 5.67% | 37.76% | 0.546 | 0.999 | 0.500 | 1.000
33 (Opt1) | 8.23 | 3.78% | 25.18% | 0.698 | 0.999 | 0.667 | 1.000
44 (Opt1) | 6.92 | 2.84% | 18.88% | 0.773 | 0.999 | 0.750 | 1.000

## Slide 13: nextline预取
Nexline预取采用miss时预取后n行的实现
使用各预取四行的设置
AMAT分别有1.18x和2.70x的提升

## Slide 14: Non-Blocking Cache
假设trace中每次请求间隔3个周期

## Slide 15: 01-mcf-gem5-xcg.trace
MSHR (L1, L2) | L1 Coverage | L2 Coverage | Avg Latency
0,0 | N/A | N/A | 16.07
1,2 | 0.19 | 0.1 | 13.65
2,4 | 0.35 | 0.18 | 11.61
4,8 | 0.57 | 0.32 | 8.26

## Slide 16: 02-stream-gem5-xaa.trace
MSHR (L1, L2) | L1 Coverage | L2 Coverage | Avg Latency
0,0 | N/A | N/A | 18.68
1,2 | 0.15 | 0.1 | 14.89
2,4 | 0.33 | 0.21 | 11.39
4,8 | 0.82 | 0.42 | 5.33

## Slide 17: Non-Blocking Cache
假设trace中每次请求间隔3个周期
采取L1 4个MSHR, L2 8个MSHR的配置
AMAT分别有1.95x和3.50x的提升

## Slide 18: Victim Cache

## Slide 19: Victim Cache Impact - 01-mcf Trace
Metric | VC Size = 0 | VC Size = 32
L1 Miss Rate | 20.05% | 20.05%
Victim Cache Hit Count | 0 | 0
Victim Cache Hit Ratio | 0.00 | 0.00
L2 Miss Rate | 39.61% | 43.30%
Main Memory Reads | 22247 | 22354
Main Memory Writes | 2535 | 1867
Total Latency | 3737713 | 3636223
Average Latency | 16.07 | 15.63

## Slide 20: Victim Cache Impact - 02-stream Trace
Metric | VC Size = 0 | VC Size = 32
L1 Miss Rate | 11.34% | 11.34%
Victim Cache Hit Count | 0 | 0
Victim Cache Hit Ratio | 0.00 | 0.00
L2 Miss Rate | 75.52% | 75.03%
Main Memory Reads | 18473 | 18473
Main Memory Writes | 4624 | 4835
Total Latency | 3043008 | 3065698
Average Latency | 18.68 | 18.82

## Slide 21: Victim Cache
没有用
LRU在当前的cache配置和测试数据上工作的很好

## Slide 22: Stride预取
根据最近两次访存的stride和方向预取

## Slide 23: 01-mcf Dataset Prefetch Comparison
Configuration | AMAT | L1 Miss Rate | L2 Miss Rate | L1 Coverage Rate | L1 Prefetch Accuracy | L2 Coverage Rate | L2 Prefetch Accuracy
11 (Base) | 16.07 | 20.05% | 39.61% | N/A | N/A | N/A | N/A
22 (Opt4) | 15.06 | 18.65% | 44.76% | 0.154 | 0.213 | 0.193 | 0.196
33 (Opt4) | 15.03 | 18.37% | 43.52% | 0.193 | 0.198 | 0.285 | 0.181
44 (Opt4) | 15.49 | 18.25% | 44.95% | 0.213 | 0.190 | 0.346 | 0.158

## Slide 24: 02-stream Dataset Prefetch Comparison
Configuration | AMAT | L1 Miss Rate | L2 Miss Rate | L1 Coverage Rate | L1 Prefetch Accuracy | L2 Coverage Rate | L2 Prefetch Accuracy
11 (Base) | 18.68 | 11.34% | 75.52% | N/A | N/A | N/A | N/A
22 (Opt4) | 13.16 | 10.70% | 59.06% | 0.052 | 0.473 | 0.278 | 0.228
33 (Opt4) | 13.82 | 11.09% | 50.56% | 0.113 | 0.067 | 0.334 | 0.123
44 (Opt4) | 12.83 | 11.01% | 50.83% | 0.120 | 0.072 | 0.318 | 0.078

## Slide 25: Stride预取
根据最近两次失效的stride和方向预取
L1&L2预取4行，AMAT分别有1.04x和1.46x的提升
不如nextline

## Slide 26: Eviction Policy
通过前面victim cache的数据可以看到LRU已经满足需求，所有没有实现其它驱逐策略

## Slide 27: Cache Bypassing
实际上破坏了原本的多级缓存模型，一致性不好保证(?跳过了一个在cache中dirty的块)
难以识别局部性差的访存模式(stride prefetch可以看出访存模式并不好识别)
感觉会比较适合有信息的情况，比如编译器发现某些数据只会读一遍，用专门的指令跳过cache; 在线识别太复杂
所以没有实现

## Slide 28: 最终优化
L1，L2预取后四行
Non-Blocking Cache L1 4 MSHR, L2 8 MSHR
Overhead: 预取逻辑+额外MissRate * 3的线路带宽+12 MSHR+Non-Blocking的处理逻辑

## Slide 29
Metric | 01-mcf Trace | 02-stream Trace
L1 Total Reads | 181708 | 113651
L1 Total Read Misses | 37468 | 3081
L1 Total Writes | 50903 | 49245
L1 Total Write Misses | 3542 | 1541
L1 Miss Rate | 17.63% | 2.84%
Prefetch Count (L1) | 89027 | 13863
Prefetch Cover Count (L1) | 98865 | 125952
Prefetch Hit Count (L1) | 13296 | 13851
Coverage Rate (L1) | 0.425023 | 0.773205
Prefetch Accuracy (L1) | 0.149348 | 0.999134
Hit Under Miss (L1) | 25527 | 4622
MSHR Coverage Rate (L1) | 0.62 | 1.0
L2 Total Reads | 130037 | 18485
L2 Total Read Misses | 24113 | 4622
L2 Total Writes (L2) | 13025 | 5990
L2 Total Write Misses (L2) | 0 | 0
L2 Miss Rate | 16.85% | 18.88%
Prefetch Count (L2) | 40678 | 13863
Prefetch Cover Count (L2) | 77020 | 18353
Prefetch Hit Count (L2) | 38582 | 13863
Coverage Rate (L2) | 0.538368 | 0.749867
Prefetch Accuracy (L2) | 0.948473 | 1
Hit Under Miss (L2) | 8506 | 4621
MSHR Coverage Rate (L2) | 0.35 | 1.0
Main Memory Total Reads | 64791 | 18485
Main Memory Total Writes | 4286 | 4624
Average Latency | 6.99 | 3.0

## Slide 30: 最终优化
L1，L2预取后四行
Non-Blocking Cache L1 4 MSHR, L2 8 MSHR
Overhead: 预取逻辑+额外MissRate * 3的线路带宽+12 MSHR+Non-Blocking的处理逻辑
优化为2.30x和6.23x